## Slide 1
Calibration Reference Data System Design Perry Greenfield Science Software Branch

## Slide 2
Calibration Pipeline Component
You are here

## Slide 3: DMS Data Flow Diagram

## Slide 4
Key Requirements

## Slide 5: Original CRDS Key Requirements (1/2)
ID | Requirement
DMS-535 | The CRDS shall ensure that all reference files and information regarding the rules for mapping data to reference files are archived before the reference files or rules may be used. [level 4 req 6.4.2.2]
DMS-536 | The CRDS shall identify the most appropriate reference data to use for the calibration pipelines. [req 6.4.3.1]
DMS-537 | The CRDS shall support multiple versions of the calibration pipeline simultaneously. [6.4.3.2]
DMS-538 | The CRDS shall commit new reference files without requiring their use in operations.[6.4.3.3]
DMS-539 | The CRDS shall have a common software interface for both local and remote users.[6.4.3.4]
DMS-540 | Outside users shall be able to query the CRDS through a web interface for the most appropriate reference files for the specific version of a calibration pipeline and a particular data set. [req 6.4.3.5]
DMS-541 | The CRDS shall have the capability to recreate the list of appropriate calibration reference files for any point in the past given the date of the query, version of software, and a specific data set. [req 6.4.3.6]
DMS-542 | The CRDS shall record meta data about the reference files and all information regarding how data sets are matched to reference files including (but not limited to): [req 6.4.3.7] 1) How the reference file was generated (or links to documents regarding that), 2) Who created the reference file, 3) Who committed the reference file, 4) Information about the significance of the change.

## Slide 6: Original Key CRDS Requirements (2/2)
ID | Requirement
DMS-543 | It shall be possible to mark committed reference files as bad so they will no longer be selected by CRDS. [req 6.4.3.8]
DMS-544 | Rules describing how reference files are matched to data and software versions shall be separate from the reference files. [req 6.4.3.9]
DMS-545 | A tool shall be provided that will list where differences exist for recommended reference files between two rules and list of data sets. [req 6.4.3.10]
DMS-546 | Reference files shall include in their headers information in the form of header comments that describe the procedure for making the reference file or point to a reference that describes that procedure. [ref 6.4.3.13]
DMS-547 | CRDS shall provide a tool to show the set of active reference files being used for all supported versions of the software, or a specific version of the software. [ref 6.4.3.14]
DMS-548 | CRDS shall provide a tool to show active files associated with specific instrument observing modes. [ref 6.4.3.15]
DMS-641 | CRDS shall have the capability to mark a specific rule as bad so as to prevent its use by the CRDS. [ref 6.4.3.12]
DMS-642 | CRDS shall have the capability to undo the use of a specific rule mapping data to a reference file. [ref 6.4.3.11]

## Slide 7
Operations Concept

## Slide 8: CRDS Ops Concept
Key CRDS functionality
  Identify the most appropriate calibration reference data for a data set based on science instrument, mode, and date.
  Check the validity of calibration reference data files
  Track when and why calibration reference data have been entered into the system.
  Ensure that calibration reference data are appropriately archived.
  Provide user access to calibration reference data information.
Analog to HST CDBS
  CDBS design precludes easy implementation of all desired requirements.
  New architecture required.

## Slide 9
DMS pipelines: The sequence of operations DMS applies to all data, starting with telemetry
Calibration pipelines: One of the tasks part of the DMS pipelines specifically for the purposes of calibrating the data.
Reference Files: Files used by calibration pipelines to apply calibration corrections. Examples:
  Flat fields
  Darks
  Geometric distortion model
Glossary

## Slide 10
Mapping rule: The specification of how a data set is matched to a specific reference file for a specific kind of reference file. Only one used per reference file type (at a time). Depends on:
  Instrument configuration
  Proposal and engineering information
  Date
  …
Context: The set of all rules in effect for a given pipeline environment.
Glossary (cont.)

## Slide 11
Allow Calibration pipelines to use directly
  Do not require user to edit data file headers to update recommended reference files
Allow Calibration pipelines to use remotely by observers at their home institutions [DMS-539]
Make mapping rules explicit to Instrument Scientists
  To make effect of changes clear
Support multiple versions of system simultaneously [DMS-537]
  Aids testing
  Required for distributed use of calibration pipelines
CRDS Operational Goals

## Slide 12
Separate reference file deliveries from mapping rules.
  Deliver reference files without any regard for how datasets are mapped to them. [DMS-544]
  Deliveries do not trigger use in pipeline or anywhere else. [DMS-538]
Entirely different approach for mapping rules.
  Must edit mapping rules in their entirety
  Minimize redundancy of information
  Examples are the best way to explain
But first, examples of use cases…
CRDS Operational Goals (cont.)

## Slide 13
Default pipeline access is through web service
  Allows pipelines run remotely (e.g., astronomer’s home institution) using exactly the same mechanism to get reference file recommendations.
  Remote (Astronomer-run) pipelines may use different pipeline versions or contexts
Multiple versions of contexts for operational pipelines can be tested simultaneously
  Sometimes necessary since instrument teams often have asynchronous schedules (use of a common test system is not adequate)
Projects can use rmap engine locally (I.e., not the web service) to:
  Use customized rmaps (e.g., they have their own reference files or different rules they prefer to use)
    E.g. Legacy projects or IDTs
  To eliminate network dependency
Use Case Drivers

## Slide 14
bestref Clients

## Slide 15
Can be used for both HST and JWST operational pipelines
HST OPUS uses bestref before calling calibration pipelines
  Preloads data headers with recommended files
JWST Calibration Pipelines will interact directly with CRDS
  No pre-loading headers with reference file names
Bestref Use Case 1: Operations Pipelines

## Slide 16
xxxx
xxx

## Slide 17
xxxx
xxx

## Slide 18
xxxx
xxx

## Slide 19
xxxx
xxx

## Slide 20
xxxx
xxx

## Slide 21
Astronomer runs pipeline at home institution
Works exactly the same way as for pipeline in operations by default
More options available:
  User may select different context than current operations use
  User may run with different version of calibration pipeline than current operations uses
  User may preload header with reference files to use
    Using a different tool that updates headers with information obtained from CRDS
    If desire is to override some CRDS choices, or run pipelines with no web access
  User may use command line switches to override CRDS recommended reference files
Bestref Use Case 2: Astronomer-run Pipeline

## Slide 22
Calibration Pipeline/CRDS high-level protocol:
  Calibration Pipeline passes augmented data header to CRDS through a web-service mechanism
  We are trying to avoid explicit coupling of specific required selection criteria in the interface. Just give it the whole header
  Augmented info includes software version and other processing environment details that are relevant; just add as extra keywords to the header passed.
  CRDS returns list of recommended reference files to calibration pipeline.
  Calibration pipeline checks to see if these reference files are present on local system.
  If not, it uses a different CRDS web service to retrieve needed files.
  Calibration pipeline opens appropriate reference file when relevant calibration step runs.
Details of Use in Calibration Pipeline (cont.)

## Slide 23
User accesses web page to obtain CRDS recommended reference files
User supplies either:
  Data file name
  Data file itself (through upload)
  Specified selection parameters (instrument, mode, date , etc)
Action is to return (depending on selected option):
  Web page with results listed
  Text file with results
  Emailed results
  Data file with updated header
Bestref Use case 3: Web Form Access

## Slide 24
User writes Python script (though web service will support any language) to obtain dictionary of reference files returned.
Easy way for user to customize pipeline software reference file handling
Bestref Use case 4: Script Access

## Slide 25
A project wants to use CRDS with their own rules or reference files.
  They install the CRDS bestref service software locally
    Bestref software is compact and portable
  They obtain relevant rmap/context files from STScI
  They modify or add their own reference/rmap/context files to have the recommendations run the way they wish
Useful for large legacy projects or IDTs that have custom pipelines
Bestref Use case 5: Local CRDS service

## Slide 26
A rules file (called “rmap”) defines all the rules in effect for a specific kind of reference file.
  E.g., MIRI nonlinearity
Aside from the software that interprets the rules, the rmap file is entirely self-contained
  No dependencies on information elsewhere
  All referenced reference files are explicitly listed in rmap files
    If it isn’t there, it doesn’t get used
  Because it is self-contained, simple to support many versions of the rules
    Each version is simply a different file
rmap files are simple ascii files, human readable
  E.g., not xml!
Types of possible rules limited only by the software that interprets them
  Current set based on experience with what is needed to support HST reference files
Defining Mapping Rules

## Slide 27
header = {
'mapping' : 'reference',
'observatory' : 'HST',
'instrument' : 'ACS',
'reftype' : 'IDCTAB',
'parkey' : (('DETECTOR',),('DATE-OBS', 'TIME-OBS')),
}
selector = Match({
('HRC',) : UseAfter({
'2002-03-01 00:00:00' : 'p7d1548qj_idc.fits',
'2002-10-21 00:00:00' : 'q692007bj_idc.fits',
}),
('SBC',) : UseAfter({
'2002-03-01 00:00:00' : 'o911150jj_idc.fits',
'2002-10-21 00:00:00' : 's5d1409dj_idc.fits',
'2007-07-17 00:00:00' : 's5f1959lj_idc.fits',
}),
('WFC',) : UseAfter({
'2002-03-01 00:00:00' : 'v4115408j_idc.fits',
'2002-10-21 00:00:00' : 'u7n18502j_idc.fits',
'2009-01-01 00:00:00' : 'u7n18501j_idc.fits',
}),
})
Example rmap file

## Slide 28
Past experience with HST indicates that most reference file types have very few active reference files
  Typically less than 20 per instrument reference file type for the great majority.
  No need for a complicated system to handle mapping these.
What about the exceptions?
  A few HST cases number > 500 active files
  All these are time-dependent data (e.g., daily darks or bias)
  For these lookups are simple (ordered data)
  For these changes are usually simple appends to the rmap file (most lines don’t change between versions)
  Even for daily reference files, updates are typically done much more infrequently (weekly at most).
  The space taken up by having 500 such updates (the approximate number of weeks in 10 years) will not lead to significant storage issues
  The elimination of OTFR means that there is not a strong need for a high update frequency as well.
In conclusion:
  There is no good reason not to save all previous mapping rules
  There is no good reason not to have instrument scientists edit the rules directly
Manageability of Rules Files

## Slide 29
HST provides a good test of practicality
  Lots of reference file types to test against
Developed code to generate rmaps automatically from currently active files
Uncovered a few cases not handled well in initial set of selecting functions
  Mainly bias files
Developed new selector constructs as a result:
  Aliases for lists of matching modes
  Pattern matching against modes
    E.g., all mode strings that contain “subarray”
Goal of new constructs is to minimize multiple appearances of reference file names in rmaps
Testing against HST Reference Files

## Slide 30
Hierarchical dependency structure
Pipeline context file lists which instrument context files are being used.
Instrument context files list which reference file mapping rules files are being used
Specifying a unique pipeline context file and version of the CRDS software, defines everything about what CRDS will use, and how it uses it.
Managing CRDS Versions

## Slide 31
header = {
'mapping': 'pipeline',
'observatory':'HST',
'parkey' : ('INSTRUME',),
}
selector = {
'ACS':'hst_acs_010.imap',
'COS':'hst_cos_034.imap',
'STIS':'hst_stis_004.imap',
'WFC3':'hst_wfc3_017.imap',
}
Example Pipeline Context File

## Slide 32
header = {
'mapping' : 'instrument',
'observatory' : 'HST',
'instrument' : 'ACS',
}
selector = {
'idctab' : ('idc', 'hst_acs_idctab_003.rmap'),
'darkfile' : ('drk', 'hst_acs_darkfile_115.rmap'),
'atodtab' : ('a2d', 'hst_acs_atodtab_002.rmap'),
'biasfile' : ('bia', 'hst_acs_biasfile_217.rmap'),
'spottab' : ('csp', 'hst_acs_spottab_001.rmap'),
'mlintab' : ('lin', 'hst_acs_mlintab_005.rmap'),
'dgeofile' : ('dxy', 'hst_acs_dgeofile_008.rmap'),
'bpixtab' : ('bpx', 'hst_acs_bpixtab_003.rmap'),
'oscntab' : ('osc', 'hst_acs_oscntab_022.rmap'),
'ccdtab' : ('ccd', 'hst_acs_ccdtab_005.rmap'),
'crrejtab' : ('crr', 'hst_acs_crrejtab_011.rmap'),
'pfltfile' : ('pfl', 'hst_acs_pfltfile_013.rmap'),
'cfltfile' : ('cfl', 'hst_acs_cfltfile_009.rmap'),
'mdriztab' : ('mdz', 'hst_acs_mdriztab_027.rmap'),
}
Example Instrument Context File

## Slide 33
Easy to add new kinds of mapping rules
Mapping rules are explicit and all in one place
  Simple to compare different versions
Supports multiple contexts
  Different pipelines can run different versions of CRDS simultaneously
Bestref functionality is portable
  Easily distributed and run by users or other institutions
Capabilities Permitted

## Slide 34
Make new reference file(s)
Validate/deliver reference files
Update corresponding reference mapping file
Validated/deliver new mapping file
Update/deliver context files:
  corresponding instrument context file
  pipeline context file
Test new pipeline context file in operations test environment
Update pipeline to use new pipeline context file
Process for Delivering and Using New Reference Files

## Slide 35
Deliveries involve:
  Providing necessary provenance information [DMS-542]
  Validation of reference/rmap/context files
  Assigning/validating a name for the file
  Archiving the file
  Updating the catalog of reference/rmap/context files with all relevant information.
Delivering Reference/rmap/context Files

## Slide 36
xxxx
Commiting Files to CRDS

## Slide 37
IS/RIA/RIS:
  commits new reference files
  edits rmap to use new reference files
  commits new rmap file
  edits instrument context file to use new rmap file
  commits new instrument context file
  edits pipeline context file to use new instrument context file
  commits new pipeline context file
  requests operations test new pipeline context
Operations:
  sets test version of operational environment to use new pipeline context, runs regression tests
  on approval from WIT, sets operations environment to use new pipeline context
Commit Use Case 1: General Case

## Slide 38
Used when there is one-for-one file replacement (reference, rmap or instrument context) for any number of files listed within one file.
Web form allows entering in replacements for listed files.
One button submit handles chain of commits. E.g.,
  Commits all reference files
  When reference file commits complete, creates new rmap, then commits that
    Replaces old rmap entry reference file names with the identified committed reference files
  When rmap commit completes, creates new instrument context, commits that
    Replaces old instrument context rmap reference with new rmap name generated
  When instrument context completes, creates new pipeline context, commits that
    Replaces old pipeline context instrument context reference with new instrument context name generated
  Returns names of all committed files
Commit Use Case 2: File replacement

## Slide 39
Adding new time-dependent reference files to existing list in rmap
Web form provides place to make additions to existing rmap file
Goes through same process as Use Case 2 to edit/commit all chained files
One step for the user
Commit Use Case 3: time-dependent changes

## Slide 40
For all types of files:
  Name must be unique and obeys naming conventions
    CRDS supplies name, retains original name in catalog and header
  Information must be provided to document provenance: [DMS-542]
    Who made the file, who committed the file
    How the file was made, etc
    Significance of change
Reference Files:
  Verify file is conformant with required format (e.g. valid FITS file)
  Verify file contains necessary information on how the file was generated [DMS-546]
  Verify file has necessary structure and content
    Very open ended
    Lots of rules on content make for harder maintenance
Rules Files:
  All reference files referred to must be in CRDS [DMS-535]
  Syntax is correct
  All previous modes covered remain covered [provide warning]
  No identical selection sets can appear twice in the file.
Context Files:
  All context or rules files referred to must be in CRDS [DMS-535]
  Syntax is correct
Validation of CRDS Files

## Slide 41
The archive shall be able to archive the following kinds of files:
  Calibration Reference Files
  Rules Files that define how data should be mapped to Calibration Reference Files
  Context Files that define which Rules Files should be used for a given instance of calibration pipeline execution
The Archive shall accept any name supplied for such files, and any format provided.
  The Archive shall be able to apply a set of rules for the acceptable name and format of the file to be archived. These rules shall be configurable to handle new naming schemes or a new file format if one is added to the supported list
The archive shall provide a mechanism to prevent the overwriting of a reference/rmap/context file with the same name by CRDS when CRDS submits such a file to the archive to be archived
Requirements CRDS places on Archive

## Slide 42
xxxx
Utilities Use Categories

## Slide 43
Software Design

## Slide 44
CRDS will be written entirely in Python with the following exceptions:
  Any C code needed to enhance performance (viewed as unlikely)
  Javascript and related tools needed within web forms for user interface interactivity
    Jquery
    DHTML
Web interactions will use the Django web framework
  Most widely used Python web framework
    django-json-rpc module
  Will use Apache as web server
MySQL will be the database used for the file catalog
  Integrates well with Python, and already used by ETCs, will share same database server
CRDS Design: Languages/Tools

## Slide 45
Bestref service
  Basic capability implemented
  Basic functionality running on test web server
  Performance capable of handling hundreds of requests (all reference files) per second on HST examples
Commit functionality
Utilities for
  Operators
  Operational Software
  Instrument scientists
Areas of Design/Development

## Slide 46
HST project has approved adoption of CRDS for HST use within the next two years
Providing funding for implementation and testing
HST needs closely aligned with JWST
  Requirements effort underway
  Almost all proposed HST generated requirements useful for JWST as well
  HST rules and reference files have already been used for initial testing
JWST will benefit from near-term testing in a production environment
Biggest additional effort will come from software needed to automatically generate rmaps from existing CDBS information
Main testing will be to compare CDBS bestref results with CRDS bestref results on large numbers of data sets
Coordinated Development with HST

## Slide 47
Design very straightforward
Provide pipeline context as top-level pointer to nested file dependencies.
Use these to load all relevant rmap files
Each rmap file is parsed to build data structure that is used to successively select subgroups of reference files until all selection criteria are used to isolate to one reference file.
Service is always provided “dictionary-like” input data (e.g., keyword/value pairs)
  FITS headers for example
  Avoid defining specific selection parameter lists for each instrument
    Makes changing selection criteria easier if whole headers are submitted to service
  Data file headers will likely need a few extra items inserted for proper lookup.
    E.g, version of calibration pipeline software
Wildcard matches may overlap with more specific matches. More specific match is always chosen over wildcard match
Uses Python dictionary structure heavily for implementation (high performance lookup)
Bestref Design Decisions

## Slide 48
Web interface requires authentication
  Not just anyone should be able to commit files!
Streamlined commit facility requires significant interactivity on web form
  Hence javascript technology
Adoption of CDBS TPN files for validation
  These files describe properties of reference files that should be met
  Can use these (or something similar) for JWST validation information
  Includes expected data structure (for tables), data type, required keywords, columns in tables, etc.
Interface issues with Archive
  How to submit files to the Archive (current and future)
  How to monitor process in archiving files
Commit Design Decisions

## Slide 49
File naming issues
  Ensuring unique names
  Naming convention for reference/rmap/context files
    Favor automatically sequentially generated filenames
Show current and recent pipeline context in user interface choices of contexts to base changes on
  Requires Operational system to maintain history of contexts used and provide interface to CRDS (and other systems) for obtaining the history
Detect and warn when rmap update eliminates a previously existing selection case
  Likely a user error
  Listed under utilities as well
Commit Design Decisions (cont)

## Slide 50
(Not a complete list)
General Utilities (useful for more than one category)
  Synchronize local reference file directories to contain all reference files required by given list of pipeline contexts
    Useful for Operations, WIT, and other projects (e.g., IDTs)
  Highlight all differences in rules and reference files between rmaps, instrument contexts or pipeline contexts
Utilities Design

## Slide 51
Operational System Utilities
  Detection of reversion of reference, rmap, or instrument context files when changing pipeline context
    Prevents inadvertent undoing of previous updates by uncoordinated modifications
  Get list of datasets affected by pipeline context change
    Useful for identifying data sets needing reprocessing
    Design Issue: Some table reference files have rows selected by additional selection criteria. A change to the file does not necessarily affect all data sets that use that reference table. This utility must examine the contents of these tables to determine which data sets are affected (and store the selection criteria for the rows in rmaps for this utility to use in doing such checks)
    Design Issue: Selection based on severity of change of reference file change. Some desire the ability of selecting only data sets for which the change in reference files is considered to be above some specified threshold (e.g., moderate, or severe).
      Very difficult problem to do correctly and make practical
      Few successful examples in past
        Actually, none (?)
      Still an open issue
      Awaiting well defined concept for how this should work before accepting as a requirement
Utilities Design (cont)

## Slide 52
WIT Utilities
  What data sets or contexts use a given reference file
  Mark reference file as bad
  Show what selection criteria use a given reference file
  Show if an rmap update doesn’t cover a selection case covered in the previous version of the rmap (likely folded into commit user interface), or changes the set of selection criteria
  Show current operational configuration
  More sophisticated reference file comparison tool
    E.g., capable of detecting insertions or deletions of rows in tables between two versions
Utilities Design (cont.)